## Slide 1
EE4404 Project
Group member：
Wu Shuye
Kan Ziyang
Wu Junxi
Liao Yiming
The Utilization of Shared Energy Storage in Energy Systems
A Comprehensive Review
U2401022
U2401026
U2401029
U2401115

## Slide 2
Energy storage sharing architecture
01
CONTENTS
Realization of shared energy storage
Modeling and optimization of energy storage sharing
Literature Classification
Introduction
Future Research Directions
Background and significance
Summary
02
03
04
05
06
07
08

## Slide 3
Introduction
LED
Today, our group will give a presentation on the application of shared energy storage (SES) in energy systems. Our report is based on the paper which written by Rui Dai, Rasul Esmaeilbeigi and Hadi Charkhgard, and published in IEEE TRANSACTIONS ON SMART GRID.
The article mainly introduces the concept, architecture, implementation, modeling and optimization methods of shared energy storage, classifies and compares related literature, and explores future research directions.
● According:

## Slide 4
Background and significance
Energy storage plays an important role in modern smart grids and energy systems. It can improve system efficiency and resilience, achieve energy arbitrage, and ensure stable power generation from renewable energy.
● Background:

## Slide 5
Background and significance
However, it faces challenges in system framework design and management strategy development. Shared energy storage has attracted attention due to the increase in energy exchange in energy systems. It can overcome the limitations of traditional energy storage utilization frameworks and bring new economic opportunities.
● Background:

## Slide 6
Background and significance
● Scope of the study:
Concepts related to energy storage sharing are explained, including users, capacity sharing and storage energy sharing, implementation methods of shared energy storage (direct and indirect), fairness and efficiency, etc.

## Slide 7
Background and significance
● Literature collection method:
Through the Scopus database, specific keywords were used to search for papers related to shared energy storage in the past ten years. After screening, 281 papers were obtained, of which 67 were related to direct energy storage sharing. This paper mainly reviews these papers.

## Slide 8
Background and significance
● Contributions and outline:
Systematically review the research on shared energy storage, classify the shared energy storage architecture and explain the advantages and disadvantages, review and classify related papers from multiple aspects, point out the gaps in the literature and provide research directions.

## Slide 9
Energy storage sharing architecture
● Private energy storage:
Each user owns and independently operates energy storage, which is the mainstream framework for energy trading and sharing systems, but there are problems such as cost inefficiency and difficulty in determining the scale of energy storage.

## Slide 10
Energy storage sharing architecture
● Interconnected energy storage:
Capacity sharing is achieved through interconnected users’ energy storage, and the storage capacity can be adjusted, but there are still cost issues in the distributed framework, and the management strategy focuses on incentive mechanisms.

## Slide 11
Energy storage sharing architecture
● Public energy storage:
Installing a shared energy storage for all users is the mainstream architecture, such as community energy storage. Operational strategies include allocating capacity to allow users to operate independently or coordinated and managed by aggregators, involving capacity allocation and storage energy allocation issues.

## Slide 12
Energy storage sharing architecture
● Independent energy storage:
Shared energy storage is managed by independent operators who determine the storage capacity and price of stored energy. It is suitable for markets that serve many users, such as cloud energy storage, but faces challenges such as price determination, fairness in energy distribution, and balancing conflicts of interest between operators and users.

## Slide 13
Application scenarios
LED
Providing energy storage services to multiple homes or buildings in a community or neighborhood area. This can be achieved through interconnected energy storage or public energy storage architecture, usually operated by an aggregator.
● Community energy storage:

## Slide 14
Application scenarios
LED
Using cloud computing concepts and combining a variety of energy storage technologies to provide services to a large number of customers in the energy market, it is large-scale, serves a wide range of user types, and has low costs, but only achieves capacity sharing.
● Cloud energy storage:

## Slide 15
Application scenarios
LED
Built by integrating distributed energy storage units and virtualizing the allocation of storage capacity to users.
● Virtual energy storage power plant:

## Slide 16
Application scenarios
LED
The application of the sharing economy model to energy storage sharing can enable investors and operators to profit, such as companies investing in energy storage for arbitrage and residents optimizing their energy needs and storage levels.
● Business models based on the sharing economy:

## Slide 17
Integration with other energy technologies
LED
Renewable energy sources such as solar and wind power have intermittent power generation, and integration with shared energy storage can ensure a stable supply. Balancing energy storage is needed to share and support the use of renewable energy.
● Integration with renewable energy:

## Slide 18
Integration with other energy technologies
LED
Electric vehicle batteries can be used as shared energy storage or shared energy storage at charging stations, such as using retired batteries to support charging stations, Tesla sharing energy storage at charging stations, etc.
● Integration with electric vehicles:

## Slide 19
Practical applications and case studies
LED
Actual projects include SMUD's Energy StorageShares, Tesla's ConnectedSolutions, and the EU’s SHAR-Q, connecting distributed energy storage for virtual power plants and sustainable energy supply.
● Actual projects:
● Case studies:
Case studies cover community and cloud energy storage evaluations, including UK and Germany's economic assessments, feasibility analyses, and the benefits of shared energy storage compared to other systems.

## Slide 20
Modeling and optimization
of energy storage sharing
LED
● Management Strategies for ES Sharing:
• Game theory model:
Game Theory is a theoretical framework to study the interactions among the competing players. It can be employed to model the conflicts among the users of ES sharing.
Benefit
Fairness
non-cooperative model
independent decisions
cooperative model
joint decisions
energy consumption
battery capacity allocation
Optimize

## Slide 21
Modeling and optimization
of energy storage sharing
LED
● Management Strategies for ES Sharing:
• Auction model:
Users obtain energy storage resources through competitive bidding to ensure fair sharing of capacity and energy.
• Capacity allocation model:
ES sharing can also be studied as a resource allocation problem by allowing the capacity of the shared ES to be separable. Such models first determine how to allocate the capacity of the shared ES to each user. Then the users independently operate their portion of the ES capacity without exchanging their stored energy.
• Pricing model:
Ensure fairness through appropriate pricing mechanisms and incentivize users to participate in energy storage sharing.

## Slide 22
Modeling and optimization
of energy storage sharing
LED
● Determining the scale of shared energy storage:
The appropriate scale of energy storage can reduce costs. Capacity and energy sharing factors need to be considered in shared energy storage systems.
Using random methods or planning models based on the sharing economy to determine the scale of shared energy storage.
LED
● Shared energy storage control:
Develop control strategies to achieve real-time energy management, optimize charging and discharging, coordinate energy storage sharing among different entities, use reinforcement learning to control energy storage, reduce grid congestion, etc.

## Slide 23
Modeling and optimization
of energy storage sharing
LED
● Multi-objective optimization:
Apply multi-objective optimization frameworks to solve multi-conflicting objective problems in shared energy storage systems, such as collaborative decision-making frameworks, bi-objective mixed integer linear programming, and multi-objective optimization techniques.
● Uncertainty handling:
Uncertainty is crucial to energy storage sharing management. It includes three forms: random, robust and fuzzy. Currently, fuzzy and uncertain programming have not been applied in energy storage sharing and are future research directions.

## Slide 24
LED
Architectures
  Interconnected: Show connection diagram. In small communities, users share idle capacity. It reduces cost by using existing equipment but has complex coordination.
  Common: Present layout of community storage. In large residential areas, it enables centralized management. It needs large initial investment.
Sharing Types
  Capacity: Use bar chart to show differences with comprehensive sharing. In industrial parks, enterprises allocate standby capacity.
● Architectures & Energy Sharing Types
Literature Classification
–System Design Dimension

## Slide 25
Literature Classification
–System Design Dimension
LED
Scenarios
  Cloud: Display multi-layer architecture. It has a large market share and diverse services compared to others.
  Community: show community layout with storage facility and energy transmission lines. It reduces community electricity cost.
● Application Scenarios & Energy Integration
Energy Technologies
  Renewable (R): Present schematic of combination with storage. Explain how it achieves stable power supply.
  Local Generation: Illustrate connection with storage. Describe its role in ensuring power supply for critical loads.

## Slide 26
Literature Classification
- Modeling and Optimization Technology Dimension
LED
Fairness and Decision Frameworks
  Capacity Allocation: Provide flowchart. It allocates based on demand proportion or priority.
  Pricing: Display models and curves. It motivates user behavior.
Decision Frameworks
  Cooperative Game: Use case to show cost and benefit changes. Present game tree for decision and allocation.
  Non-cooperative Game: Use scatter plot to compare efficiencies. Analyze limitations like resource waste.
● Fairness and Decision Frameworks

## Slide 27
Literature Classification
- Modeling and Optimization Technology Dimension
LED
Mathematical Formulas
  Multi-level/Stage: Show timeline with decision points. Present formula evolution.
  Multi-objective: Use radar chart for weight distribution. Explain solution ideas.
Solution Technologies
  Solvers/Algorithms: List common ones and evaluate effects.
  Custom: Highlight innovations and define applicable scenarios.
● Mathematical and Solution Technologies

## Slide 28
Future Research
-benefit expansion and technology innovation
LED
    For benefit expansion, the quantification of peak shaving and the enhancement of energy storage resilience are studied through curve overlay and chart analysis respectively.
● Benefit Expansion

## Slide 29
Future Research
LED
    In the aspect of non-battery storage technologies, schematic diagrams will be presented to illustrate their principles. Subsequently, a sharing framework will be designed to integrate them into the existing system. For mobile storage, an animation will be utilized to vividly demonstrate the energy flow process. A sharing mechanism flow will be carefully designed, and the application points of technologies for enhancing efficiency will be listed. This will open up new possibilities for the development of shared energy storage.
● Technology Innovation

## Slide 30
Research Summary
LED
The research review part will display a mind map that clearly organizes the key concepts related to shared energy storage. Additionally, a keyword cloud will be presented to showcase the prominent research topics. In terms of value and outlook, data charts will be employed to assess the potential growth of shared energy storage. A roadmap will be provided to guide future research directions, indicating the steps and focuses for further exploration.
● Review and Outlook

## Slide 31
THANKS